Final Project Report
Alexander Creznic
Southern New Hampshire University
CS-350 Emerging Sys Arch & Tech
Professor Roland Morales – Information Technology Adjunct Faculty
April 17, 2025

Final Project Report
Introduction
The smart thermostat project shows the use of embedded systems and external, peripheral devices for temperature temperature. This product supports multiple hardware architectures, including the Raspberry Pi, Microchip (e.g., PIC32), and Freescale (e.g., i.MX series). Each of these supported devices has differing means for talking to peripherals and cloud connection.
Peripheral Support Across Architectures
This thermostat interacts with several components: a red LED, blue LED, a 16x2 LCD display, an AHT20 temperature and humidity sensor, and three buttons. On the Raspberry Pi, GPIO pins are used directly through the Rpi.GPIO or gpiozero libraries in Python, giving simple and direct control over LEDs and buttons. The I2C protocol allows communication with the AHT20 sensor and the LCD display.
The Microchip architecture, like the PIC32 series, supports similar components with its I/O ports and onboard communication modules. Interfacing with the AHT20 sensor over I2C requires configuring I2C registers and writing appropriate device drivers (Microchip Staff, 2024). Microchip’s MPLAB X and Harmony framework simplify some of these processes.
Freescale’s I.MX processors – commonly used in more complex, embedded Linux systems – give great peripheral support. Like the Raspberry Pi, Freescale systems can use Linux-based drivers for I2C and GPIO, allowing the use of user-space (outside of the kernel) applications to control sensors and displays (NPX Staff, n.d.). Although, low-level interaction might still need some driver configuration or kernel modules, especially for the critical tasks.
Wi-Fi and Cloud Connectivity
All three architectures have different paths to Wi-Fi and cloud integration. The Raspberry Pi has built-in Wi-Fi and supports modern networking (Truncale, 2021). With Python libraries like requests or MQTT clients, it can easily send data to cloud services or custom REST APIs.
Microchip microcontrollers typically require external Wi-Fi modules, such as the ESP8266 or RN171, connected over UART or SPI (Nabto Staff, n.d.). Libraries and middleware provided by Microchip allow basic HTTP or MQTT communication, but cloud integration needs a more manual setup compared to the Raspberry Pi.
Freescale’s i.MX architecture supports onboard Wi-Fi or external modules, and it benefits from running a full Linux distribution. Like the Pi, it supports cloud connectivity using standard protocols. Advanced use cases like edge computing or containerized services are also possible due to its higher greater power and compatibility with modern cloud platforms.
Architectural Capabilities and Code Support
Each architecture supports the thermostat’s logic in different ways. Raspberry Pi gives users a full Python environment (Truncale, 2021), making it easy to prototype and manage multithreaded applications like the display manager and temperature monitor. Aside from threading, it supports event handling and has well established libraries for hardware access.
Microchip's PIC32 uses C and offers real-time performance with precise control over timing and I/O. It is ideal for low-power and deterministic applications. A drawback, however, is that it requires a more complex setup and lacks high-level abstractions (Microchip Staff, 2024), making development more involved.
Freescale’s i.MX series supports both high-level application development and real-time processing through a multicore architecture. Developers can split tasks across these cores or use embedded Linux (NPX Staff, n.d.). for managing complex peripherals and network tasks, all while reserving real-time functions for a dedicated core.
Conclusion
In conclusion, the thermostat project is adaptable across all three architectures. Raspberry Pi is optimal for rapid development and prototyping; Microchip excels in resource-constrained, real-time environments; and Freescale offers a balanced platform for complex, scalable embedded systems. Understanding how each architecture supports peripherals, Wi-Fi, and code execution deepens appreciation for embedded system design and implementation.

References
Microchip Staff. (June 6, 2024). Developing applications with MPLAB Harmony v3 software framework for MPUs. Microchip Developer Help. https://developerhelp.microchip.com/xwiki/bin/view/software-tools/32-bit-harmony-v3/.
Nabto Staff. ESP8266 for IoT: A complete guide. Nabto Blog. https://www.nabto.com/esp8266-for-iot-complete-guide/.
NPX Staff. (n.d.). Embedded Linux for I.MX applications processors. NPX Design. https://www.nxp.com/design/design-center/software/embedded-software/i-mx-software/embedded-linux-for-i-mx-applications-processors:IMXLINUX.
Truncale, J. (March 1, 2021). Build a home thermostat with a Raspberry Pi. OpenSource. https://opensource.com/article/21/3/thermostat-raspberry-pi.